## Slide 1
Background image from: https://upload.wikimedia.org/wikipedia/commons/e/ef/ISS-42_New_Zealand_in_Sunglint,_large_resolution.jpg
A Smart Energy Monitor
James Ashworth
Adil Bhayani
Savi Mohan
Mark Yep
Lecturers:
Muhammad Nadeem
Duleepa Thrimawithana
Background
ELECTENG 209 is an electronics design paper, taken in the second semester by every second year Electrical and Computer Systems Engineering student. The goal of this years project was to design and develop a wireless energy monitor to measure and display the amount of energy consumed by a household appliance in a smart house. Due to safety reasons, each group designed and developed a proof of concept project, which works as a scaled down system.
ELECTENG 209 Smart Energy Challenge Group 37
Smart Energy Challenge
As an extension of the regular project, the lecturers offered an optional Smart Energy Challenge. In this extension groups were required to read and graph the real time energy readings on a computer.
Additionally, our group decided that we wanted to make our Smart Energy Challenge extension truly smart. This lead us to develop an Android application for use on Android based smartphones.
Prototype Specifications
The proof of concept prototype that we created is able to work with the following specifications:
Source Voltage: 12 to 14 Vrms
Source Frequency: 500 Hz ± 10%
Maximum Load: 8.5 VA
Additionally our project features:
Voltage and current sensing circuits
Signal conditioning circuits
Digital processing and calculation system
(Atmel AVR Microcontroller based)
Wireless Radio Frequency UART
Digital base station display system (CPLD based)
Python real time graphing
Firebase real time database
Android real time graphing
System Flowchart
Microcontroller
CPLD
Computer
Firebase
Android App
UART
RS232
Wi-Fi
Wi-Fi
V
I
(From Analogue Circuit)
Seven Segment Display
Graphing
Console
Graphing
Latest Data
(On Computer Screen)
(On Smartphone Screen)
Microcontroller measures V and I through ADC
Data is sent to CPLD via Radio UART
CPLD receives UART and displays on seven segment display
CPLD sends data to laptop via serial RS232
Python reads serial data, displays on console, and graphs in real time
Uploads to Firebase
Receives data in real time from Python
Stored as Key: Value pairs, each value is encoded in JSON
Receives real time data from Firebase
Displays current data
and real time graphing
Figure 1: The analogue PCB with the Atmel Xplained Mini, CPLD, and RF modules
Technologies and Frameworks
Throughout our entire project we utilised many current frameworks and technologies. These include:
Analogue Circuit Design
  LTSpice
  Altium
Version Control System
  GitHub
Microcontroller C
  Atmel Studio
VHDL
  Altera Quartus
Python
  RS232 serial data – pySerial library
  Real Time Graphing – matplotlib library
  Firebase – Firebase library
Firebase
  JSON
  Google Requests
Android App
  Android Studio
  Firebase dependencies
  Google Requests dependencies